Hippunfold processing and layerification of subregions

Hippunfold can be used either with UNI MPRAGEized.nii.gz file or the short inversion T1 image (INV1). We recommend the latter. If you decide for the first option, you can simply feed the UNI MPRAGEized.nii.gz (output of the preprocessing pipeline) to hippunfold using this command
singularity run -e khanlab_hippunfold_latest.sif Documents/HUinput/ Documents/HUoutput_T1based participant -p --cores all --modality T1w
Note that hippunfolde is called from a container, in this case singularity.
To use the INV1 image as hippunfold input, you need to first do bias-field correction and then remove thermal noise from it. To do so, open MATLAB, cd to your anat folder and run this command:
presurf_INV2('MP2RAGE-INV1.nii.gz')
it’s OK to pretend that the input to the above command is INV1 and not INV2 image. Note that Presurfer package (https://github.com/srikash/presurfer) needs to be added to your MATLAB path. This will generate a folder called ‘presurf_inv2’ with multiple outputs of which we will need *_INV1_biascorrected.nii. For your reference, you can later rename the folder to ‘presurf_inv1’ to avoid future confusion. To do the denoising load the attached ‘BM4D_setting.mat’ structure in MATLAB. It contains several parameters for running the BM4D denoising script e.g. if the data should have Gaussian or Rice distribution, noise standard deviation, etc. You also need to have ‘bm4d’ script added to your MATLAB path that is located in reconstructionPipeline/externalTools/denoise/BM4D/bm4d.m. Then load the recently generated bias-corrected image with and without volume information. Having 1 in ‘load_nifti’ function will skip the volume info. This function is from Fresurfer and should be in your path already if not add it to path. It is located in ‘/usr/local/freesurfer/matlab/load_nifti.m’. Then we run the denoising command using ‘[y_est, sigma_est] = bm4d(z.vol, settings)’ where y_est will be the new nifti volume and sigma_est is the standerd deviation values. At the end, save ‘y_est’ as volume of your z1 and save it as a new bias corrected and denoised image.
- load('BM4D_settings.mat')
- z = load_nifti('MP2RAGE-INV1_biascorrected.nii')
- z1 = load_nifti('MP2RAGE-INV1_biascorrected.nii',1)
- [y_est, sigma_est] = bm4d(z.vol, settings)
- z1.vol = y_est;
- save_nifti(z1,'MP2RAGE-INV1_biascorrected_BM4D.nii')
At this stage, you are ready to run hippunfold using this command
singularity run -e khanlab_hippunfold_latest.sif Documents/HUinput/ Documents/HUoutput_T1based participant -p --cores all --modality T2w
Where we fool hippunfold by telling it that the input is T2-weighted but that is not the case. Hippunfold generates multiple folders of which ‘anat’ and ‘surf’ are the most important ones. You will then use Viktor’s layering code to generate bins aka layers in each subregion. The code is called ‘VPF_create_hippocampus_layers’ and requires the following arguments. N_layers is number of bins, I provide 30, 20 bins in the subregions and 10 bis extended into the SRLM i.e. [20, 10]. T1_path is the path to your processed T1 image in the ‘anat’ folder of hippunfold, i.e. sub-00*_desc-preproc_T2w.nii'. Surf_path is the path for Hippunfold ‘surf’ subfiolder where the code will call inner, outer and midthickness surfaces. Rule is the label of segmented subregions by hippunfold. I use 2 and 4 (in string format) represnting CA1 and CA3. Sampled_image is your 4D nii EPI file that has been aligned to anatomy and is also upsampled to anatomy space (* _anatomyAligned.nii.gz from the preprocessing pipeline). Since the script calls SPM, I split the 4D image into multiple 3D volumes.
layers=VPF_create_hippocampus_layers(sampled_img,subject_id,surf_path,T1_path,N_layers,rule)
This will genrate layer profiles in a 2x2 cell. The first column has 30x Y x 2 size. Where each of those 2 cells are the binning outputs per hemisphere and then 30 would be the number of bins, Y is the number of your volumes and the third dimension here shown as 2 represents each of CA1 and CA3. The second column is empty unless you enter the labeling value of DG. Note that DG is not binned because anatomically it does not consist of the layer. You can then use plot_layers_new.m to visualize layer profiles. Note this script needs to be cleaned up.